## Slide 1: Group 9
QUANTITATIVE METHODS FOR DECISION MAKING
DHL SUPPLY CHAIN
GROUP | MEMBERS
Group 9 | 5 members (names redacted for public portfolio)

## Slide 2: Scope & Problem Identification
MINIMIZE
COST
Production Cost
Shipping Cost
CO2 EMISSIONS
Objective Function: Minimizing shipping cost and keeping it within the budget.
Our objective is to reduce the shipping cost and adhere to the budget of 3 Billion CNY, considering numerous numerical budget.
Total Constraints:
Demand
Budget
Production
Route
Weight
CO2 Emission

## Slide 3: Network Diagram
LCD 32” (A)
LCD 42” (B)
ODM 1
ODM 7
ODM 6
ODM 5
ODM 4
ODM 3
ODM 2
Water (7)
Rail (6)
Road Network (5)
Road LTL (4)
Road (3)
Express Air (2)
Air (1)

## Slide 4: Mathematical Model & Lingo
Decision variables: 64 variables (A11…B27)
Objective function: Minimise shipping cost
Z = ∑ Shipping cost from A11 to B27

## Slide 5
Constraints:
Demand Fulfillment: The model must ship the exact quantity of TVs required by the client, which is 920,000 units of 42" LCDs and 530,000 units of 32" LCDs.
Budget Constraint: The total cost of the operation, including both production and shipping, cannot exceed the allocated budget of CNY 3 billion.

## Slide 6: Output & Inference
Output from Lingo:

## Slide 7: Results: Minimum Shipping Cost: 83,166,920 CNY Total Project Cost Utilized: ≤ 3,000,000,000 CNY Feasibility: FEASIBLE - The solution meets demand and all other constraints within the specified budget. Key Insights from the Optimal Solution: The optimal plan for minimizing shipping cost provides a maximum logistics efficiency of 83,166,920 CNY. This is achieved by a specific allocation of orders. The chosen plan successfully meets the required demand for all 1,450,000 TVs. Only A47, A77, and B17 have nonzero values. A47 = LCD42" from ODM4 by water (12,767.89 units) A77 = LCD42" from ODM7 by water (907,232.1 units) B17 = LCD32" from ODM1 by water (530,000.0 units) In our current solution, water is indeed the best transport mode according to your cost structure and constraints.
Inference

## Slide 8: Thank You!